## Slide 1
Selection of restoration measures
General principles and approaches Potential restoration measures Effects on river morphology and biota
Jochem Kail, University of Duisburg-Essen
Notes: This presentation deals with the aspects that have to be considered in specific, single restoration projects for the selection of restoration measures.
Three topics will be covered:
present general principles and approaches that should be considered,
give an overview on the restoration measures that are available (catalogue of measures),
summarize what is known about the effect of these restoration measures on biota and how this may guide the selection of measures (implications for future restoration projects)

## Slide 2
  Planning cycle – steps prior to selection of measures
    How does my river work?
      Natural river type
      Reference conditions
    What’s wrong?
      What’s missing?
          Hymo assessment
          Bio assessment
      What’s the reason? Why?
          Identify limiting pressures
          Difficult due to multiple-pressures
    How can we improve? – select measures
  Setting the scene
Notes: Show how this topic is linked to the other presentations.

## Slide 3
  Planning cycle – two spatial and administrative levels
  Setting the scene
Figure: N. Angelopoulos
A: Programme of Measures (PoM) | B: Individual restoration projects
Catchment-scale | Catchment to reach-scale
All water bodies | Often single water bodies
Conceptual | Technical
Good chemical status is a must! | Have to work in given catchment context
Costs not limiting even in HMWB! (except less stringent environmental objectives) | Have to work given the property situation and financial constraints
Regional to national water agencies | Local river managers
A
B
Notes: As shown in the REFORM planning cycle, the selection of measures is done at two different spatial and adiministrative levels.

## Slide 4
  Planning cycle – presentation is about restoration at project level!
  Setting the scene
Figure: N. Angelopoulos
A: Programme of Measures (PoM) | B: Individual restoration projects
Catchment-scale | Catchment to reach-scale
All water bodies | Often single water bodies
Conceptual | Technical
Good chemical status is a must! | Have to work in given catchment context
Costs not limiting even in HMWB! (except less stringent environmental objectives) | Have to work given the property situation and financial constraints
Regional to national water agencies | Local river managers
A
B
Notes: As shown in the REFORM planning cycle, the selection of measures is done at two different spatial and adiministrative levels.

## Slide 5
    1
    General principles and approaches

## Slide 6
  Holistic vs. sectoral
    Apply river restoration in the broader context of river management
    Consider the different claims to rivers
    Conflicts (e.g. restoration vs. agricultural use), but also…
    Synergies (e.g. restoration and flood protection, eco-services in general)
    Stakeholder involvement, public participation
Photos: Hydrotec, BUND
Conflicts
Synergies
  General principles and approaches
Notes: Much easier to involve stakeholders in the planning phase prior to restoration, to take their concerns into consideration. Restoration projects are usually much easier to implement if they are supported by the local stakeholders.
A colleague always says: You have to talk, talk, and talk

## Slide 7
  Catchment vs. reach-scale restoration
    Apply river restoration in a catchment context
    Multiple pressures at different spatial scales  must be considered
    Large-scale pressures (e.g. land use) can constrain reach-scale restoration
    Hierarchy: Water pollution, nutrient / fine sediment, hydrology, morphology
  General principles and approaches

## Slide 8
  Processes vs. forms
    Passive restoration: Restoring natural channel dynamics
    Active restoration: Building channel features
    Favour passive over active but not applicable in all reaches (e.g. altered morphogenic flows, sediment deficit, cohesive banks)
Passive restoration (processes)
Active restoration (forms)
Photo right: Patt et al. 1998
  General principles and approaches

## Slide 9
  Processes vs. forms
    Passive restoration: Restoring natural channel dynamics
    Active restoration: Building channel features
    Other pros and cons of the two approaches:
cost, applicability (restrictions!)
sustainability, time to reach natural state
Passive restoration (processes)
Active restoration (forms)
  General principles and approaches

## Slide 10
  Biologically relevant vs. esthetically pleasing
    New or limiting habitats created?
    See things from a fish’s or invertebrate’s perspective!
Biologically relevant (if limiting)
Esthetically pleasing (effect?)
Photo right: Wallpaper.com
  General principles and approaches

## Slide 11
  Bottlenecks vs. unspecific measures
    Bottlenecks addressed?
    Consider Liebigs “Law of the minimum”
Figure: Wikipedia
  General principles and approaches

## Slide 12
  Adaptive management
    Not (yet) possible to predict the effect of restoration
    Necessary to monitor restoration effect
    Adapting measures if necessary
Figure: N. Angelopoulos, http://www.for.gov.bc.ca
  General principles and approaches

## Slide 13
    2
    Restoration measures

## Slide 14
  Restoration measure are applied at different spatial scales
    Pressures at different spatial scales  measures at different spatial scales
    Catchment scale
    River network scale
    Reach-scale
  Potential restoration measures
Notes: Since the multiple-pressures act at different spatial scales, it is also necessary to implement restoration measures at different spatial scales, not “end-of-pipe”.

## Slide 15
  Restoration measures for catchment scale pressures
    Land use change (extensification, organic farming)
    Waste water treatment
    Reduce urban runoff and peak flows
      Unsealing
      Rainwater retention and infiltration
  Potential restoration measures
Rainwater retention basins
Rainwater infiltration systems

## Slide 16
  Restoration measures for river network scale pressures
    Source populations and stepping stones
    Riparian buffer strips
    River continuity
  Potential restoration measures

## Slide 17
  Restoration measures for river network scale pressures
    Source populations and stepping stones
      Consider re-colonization potential (source population, migration barriers, dispersal abilities)
      Establish source populations and stepping stones
  Figure: B. Heitmann, modified
  Potential restoration measures
Source population
Stepping stone
Restored reach
Notes: Only species which occur or live near the restored reach can colonize the new habitats => useful to check prior to restoration if source populations of the targeted species are present in the catchment and if they can colonize the restored reach

## Slide 18
  Restoration measures for river network scale pressures
    Riparian buffer strips
      Effects
        Nutrient / fine sediment retention
        Shading / temperature
        Organic matter input (leaves, large wood)
        Habitat for aquatic (e.g. cover) and terrestrial life stages
      Biota highly related to buffer land use
      Potentially key restoration measure
      Research need!
  Photo: Ohio Department of Natural Resources
  Potential restoration measures
!

## Slide 19
  Restoration measures for river network scale pressures
    River continuity for fish BUT ALSO…
      …for sediment transport!
      Sediment input to mitigate sediment deficit – active restoration
      Dam removal
Photo: M. Kondolf
  Potential restoration measures
  Photo: France NN

## Slide 20
  Restoration measures for reach scale pressures
    Widely used / most common
    Increasing lateral extent / restrictions
      Instream
      Riparian
      Planform
      Floodplain
  Potential restoration measures

## Slide 21
  Restoration measures for reach scale pressures
    Instream (mainly to increase habitat diversity)
      Large wood and boulder placement
      Sediment input
      Create artificial bar or riffle (e.g. glides)
      Manage aquatic vegetation
      Creating habitats like cover or shallow wave-protected areas
      Remove bed and bank fixation
      …
  Potential restoration measures

## Slide 22
  Restoration measures for reach scale pressures
    Planform
      Re-meandering
      Widening / re-braiding
      Narrow over-widened channel
      Create secondary floodplain
      Initiate / tolerate natural channel dynamics
      …
  Potential restoration measures
  Middle photo: A. Lorenz
Notes: When there is even more space available, e.g. in agricultural areas (exensively used like grassland and pasture), channel planform can be restored.

## Slide 23
    3
    Restoration effect on morphology and biota
    …and implications for future projects and selection of measures

## Slide 24
  Key messages / conclusions of REFORM WP4
    01 General: Monitor and adjust your project – nobody can fully predict restoration effects
    02 Societal benefits: Restoration pays – it increases ecosystem services
    03 Organism group: Terrestrial and semi-aquatic species benefit most from restoration
    04 Measures: There is no single “best measure” but widening generally has a high effect
    05 Biological metric: Restoration results in a higher number of individuals but few new species
    05 Biological metrics: Restoration rather affects specific species or traits than increasing mere richness
    06 Habitats: It is important to restore specific habitats not necessarily mere habitat diversity
    07 Project size and age: Small restoration projects work but better act big and long-term
    08 Catchment characteristics: Slightly higher effect in gravel-bed mountain rivers / low land-use pressure
  Restoration effect

## Slide 25
  01 General
    Monitor and adjust your project - nobody can fully predict restoration effects
      Mainly info on simple metrics (richness, diversity) – objective?
      Contrasting results
  Restoration effect
No effect
Positive effect
Notes: There are mainly studies on the effect of restoration on simple biological metrics like richness and diversity. However, the mere increase of the number of species is not tantamount to an ecological enhancement, not really the main objective of river restoration.
sensitive, near-natural community
Therefore, future studies should focus on functional metrics / traits (as mentioned by Nicolai).
Moreover, the studies reported contrasting results

## Slide 26
  01 General
    Monitor and adjust your project - nobody can fully predict restoration effects
      Mainly info on simple metrics (richness, diversity) – objective?
      Contrasting results
      Meta-analysis: high variability, ~no or negative effect
  Restoration effect
Kail et al. (2015)

## Slide 27
  02 Societal benefits
    Restoration pays – it increases ecosystem services
      Few studies (research need!)
      Restoration increases ES (total economic value)
      Depends on assumptions?
    Select measures to maximise overall benefit
  Restoration effect
Acuña et al. (2013), Vermaat et al. (2015)
Notes: TEV = total economic value (actually partial TEV since not all ecosystem services were considered)
Acuna et al. (2013): Reach-scale partial TEV is given for the four study reaches (numbered 1 to 4). The partial TEV of the restored reaches is 10-100 times the partial TEV prior to restoration.

## Slide 28
  03 Organism group
    Terrestrial and semi-aquatic species benefit most from restoration
      Higher richness (short term, few years)
  Restoration effect
Floodplain vegetation
p < 0.01
Degraded Restored
Ground beetles
p < 0.01
Degraded Restored
Macrophytes
p < 0.01
Degraded Restored
Fish
p < 0.01
Degraded Restored
Macroinvertebrates
n.s.
Degraded Restored
Jähnig et al. (2009)

## Slide 29
  03 Organism group
    Terrestrial and semi-aquatic species benefit most from restoration
      Higher richness (short term, few years)
  Restoration effect
Kail et al. (2015)

## Slide 30
  03 Organism group
    Terrestrial and semi-aquatic species benefit most from restoration
      Higher richness (short term, few years)
      Mainly widening projects (pioneer habitats, early successional stages)
      Long-term effects?
  Restoration effect
Ruhr near Binnerfeld R2, Germany, restored in 2009
2010
2012

## Slide 31
  04 Restoration measures
    There is no single “best measure” but widening generally has a high effect
      High effect especially on macrophytes…
  Restoration effect
Kail et al. 2015
Richness/diversity
Abundance/biomass

## Slide 32
  04 Restoration measures
    There is no single “best measure” but widening generally has a high effect
      High effect especially on macrophytes and ground beetles
      Instream measures highest effect on fish, macroinvertebrates
  Restoration effect
Januschke and Verdonschot (2015)
Ground beetle richness and diversity
Kail et al. (2015)

## Slide 33
  03 Organism group 04 Restoration measures
     Select measures for targeted organism group
     Restore natural morphodynamics to rejuvenate habitats
  Restoration effect

## Slide 34
  05 Biological metric
    Restoration results in a higher number of individuals but few new species
      Abundance/biomass > richness/diversity (fish, macroinvertebrates)
  Restoration effect
Miller et al. (2010)
(Kail et al. (2015)

## Slide 35
  05 Biological metric
    Restoration rather affects specific traits than increasing mere richness
      Fish: small rheophilic fish (abundance)
      Ground beetles: Sparsely vegetated river banks specialists
      Floodplain veg.: Helophytes (emergent but rooting in wetted soils)
  Restoration effect
Januschke and Verdonschot (2015), Göthe et al. (2015), Schmutz et al. (2015), figure summary analysis unpublished
Notes: In the figure, only biological metrics are shown for which the response ratio (effect of restoration) was significantly different from zero (Wilcoxon test) in the REFORM dataset of the 20 case-studies (each compared to a nearby non-restored section to quantify the effect of restoration as the difference restored minus degraded). Most of these metrics are functional metrics / traits.
The functional metrics/traits indicate how restoration has changed the abiotic habitat conditions and allows to infer causal relationships (other than mere species richness or diversity).

## Slide 36
  05 Biological metric
    Easier to increase abundance, difficult to establish new species
    Set realistic objectives, e.g.:
      fish richness in small mountain streams is low naturally
      re-colonization potential might be limited (source pop. missing)
  Restoration effect

## Slide 37
  06 Habitats
    It is important to restore specific habitats not mere habitat diversity
      Ground beetles: sparsely vegetated bars and banks
  Restoration effect
Januschke and Verdonschot (2015)

## Slide 38
  06 Habitats
    It is important to restore specific habitats not mere habitat diversity
      Ground beetles: sparsely vegetated bars and banks
      Macroinvertebrates: microhabitat (substrate) diversity (low effect on microhabitats may explain low effect on inverts)
     Select measures which restore specific habitats at relevant scales
  Restoration effect
Poppe et al. (2015)
Hymo: mesohabitat
Hymo: microhabitat
Verdonschot et al. (2015)
Notes: Macroinvertebrates depend on microhabitats (diversity). However, many restoration projects increase mesohabitat diversity but NOT microhabitat diversity => It might look esthetically pleasing and positive for ecologists but the microhabitats necessary for e.g. inverts are still missing!!

## Slide 39
  07 Project size and age
    Small restoration projects work but better act big and long-term
      Restoration effect does only depend on size if projects are large
  Restoration effect
Schmutz et al. (2014)

## Slide 40
  07 Project size and age
    Small restoration projects work but better act big and long-term
      Restoration effect does only depend on size if projects are large
      Restoration effect depends on project age, but no simple increase!
      Do short-term effects (pioneer stages) vanish over time?
  Restoration effect
Kail et al. (2015), Schmutz et al. (2015)
3 - 12.5y
>12.5y
<3y

## Slide 41
  08 Catchment / river characteristics
    Slightly higher effect in gravel-bed mountain rivers / low land-use pressure
      Gravel-bed > sand bed, mountain > lowlands, widening > other
      …but highly co-correlated
  Restoration effect
Januschke and Verdonschot (2015)
richness
diversity
Ground beetle
Kail et al. (2015

## Slide 42
  Further readings
    Peer-reviewed scientific literature (> 300 papers)
    REFORM WP4 deliverable D4.2 (meta-analysis)
      http://www.reformrivers.eu/evaluation-hydromorphological-restoration-existing-data
      Kail et al. (2015, Ecological Indicators)
    REFORM WP4 deliverable D4.3 (20 case-studies)
      http://www.reformrivers.eu/results/effects-of-river-restoration
      Hering et al. (2015, Journal of Applied Ecology)
      Hydrobiologia special issue (several papers)
    REFORM WP4 deliverable D4.4 (ecosystem services)
      http://reformrivers.eu/assessing-societal-benefits-river-restoration-using-ecosystem-services-approach
      Vermaat et al. (2015, Hydrobiologia)
  Restoration effect

## Slide 43
  How can we improve? - selection of measures
    Set clear, measurable, realistic objectives (given catchment and river char.)
    Identify main pressures / bottlenecks
    Select appropriate approach
      catchment or reach-scale sufficient?
      passive or active restoration?
    Select measures and consider
      river type (e.g. low dynamics with cohesive banks, gravel-bed>sand-bed)
      targeted organism group (terrestrial, semi-aquatic, aquatic)
      specific habitat needs (e.g. microhabitats)
      possible constraints (e.g. source pop., water quality, hydrology, sediment)
  Summary

## Slide 44
  How can we improve? - selection of measures
    Set clear, measurable, realistic objectives (given catchment and river char.)
    Identify main pressures / bottlenecks and constraints!
    Select appropriate approach
      catchment or reach-scale sufficient?
      active or passive restoration?
    Select measures and consider river type, organism group, constraints…
    Monitoring (high variability, changes over time)
    Assess (including terrestrial groups and ES)
    Adaptive management
    Try!
  Summary